Onboard AMD N330 2.3G / N55 2.6G dual core processor

RS880M+SB820M express chipset

SO-DIMM DDR3 memory, Max. 4Gb

Integrated ATI HD4200 graphics core, supports VGA, dual HDMI and LVDS sync/async

Onboard 2 mini-PCIE slots, supports SSD/Wifi

1 RTL8111E 1000M Ethernet controllers, supports Wake On LAN

Integrated Realtek ALC662 6 channel high definition audio controller

ITX-M65_N33(N55) Motherboard Photos

1. Motherboard Front View

2. I/O Panel Front View

3. I/O Panel Side View

4. Memory Side View

| Product Model | ITX-M65 |
| --- | --- |
| CPU | Onboard AMD N550 2.6GHz dual core processor(ITX-M65_N55 configures) Onboard AMD N330 2.3GHz dual core processor(ITX-M65_N33 configures) |
| Chipset | RS880M+SB320M express chipset |
| Memory | 1 x SO-DIMM DDR3 memory slot, supports 1066/800 Mhz, Max. 4GB. |
| Video | Integrated AMD HD4200 graphics core, supports 1080P HD Supports VGA/HDMI/LVDS display output, LVDS supports dual channel 24 bit |
| Expansion Slot | 1 x mini PCI-e slot, supports wifi |
| LAN | 1 x RTL8111E 1000M Ethernet controller, supports Wake On Lan, PXE booting |
| Storage | 2 x SATA2 HDD interface 1 x MSATA slot, supports SSD |
| Audio | Onboard Realtek ALC662 6 channel high fidelity audio chip, supports MIC, line out. |
| Rear I/O Panel | 1 x 12V DC_JACK input 1 x HDMI port 1 x VGA port 4 x USB 2.0 ports 1 x RJ45 LAN port 1 x Line out(green) 1 x MIC(red) |
| Internal I/O Interface | 1 x LVDS connector, 2 x15-pin 1 x JHDMI header, same signal as HDMI 1 x JVGA header, same signal with DB15 2 x RS232 connectors 4 x USB 2.0 connectors 1 x audio connector(front panel audio port) 1 x CD-IN power amplifier connector 1 x FP1 front panel function button and indicator light header, 2 x 5-pin 1 x ATX_12V power JACK, can be +12v input and output power interface 2 x PWROUT HDD power supply connectors 1 x LVDS INVERTER connector |
| Fan connector | 1 x CPU Fan connector and 1 x System Fan connector, 3-pin |
| GPIO | Supports 4 channel GPIO |
| BIOS | AMI 8MB DPI Flash ROM |
| Watch Dog | Supports hardware reset function(256 level, 0-255 seconds) |
| PSU | DC_12V single power supply input |
| Working Temp | -10℃～60℃ |
| Storing Temp | -20℃～70℃ |
| Working Humidity | 0%-95% relative humidity, non-condensing |
| Dimension | 170mm x 170mm Mini ITX form factor |