PPC-P133-HY

13.3 inch TFT Touch Screen Embedded Industrial Panel PC powered by Intel Celeron J1900/ Core i5 4200U, 6 x COM, 2 x LAN, 4 x USB

Product description:

PPC-P133-HY is a touch panel computer solution designed for human-machine interface applications. It uses Intel® J1900 processor/Intel I5 4200U processor, onboard 4GB DDR3 memory (upgradeable), and a resolution of 1920x 1080 LCD display and full flat capacitive touch screen. The whole machine adopts 9～36V DC power supply, which effectively controls the internal heat of the computer; provides a more diversified data storage device, and supports MSATA/SSD and SATA2.5" notebook hard disks; integrates a wealth of I/O interfaces, 6 x RS232 Or 4 x RS232/2-485, 2 x 10～1000M Ethernet ports and 4 x USB3.0 ports.

PPC-P133-HY supports a variety of installation methods such as wall hanging and swing arm, which is very convenient for installation and maintenance; the front panel complies with NEMA/IP65 waterproof and dustproof standards, which can effectively control the splashing of water droplets and water vapor from the site to enter the host and affect the normal operation of the equipment Work; the equipment adopts a fanless design, limited control of dust entering the equipment, ensuring a more stable operation of the equipment, and quickly dissipating the internal heat of the system through the external surface heat sink, so that it can adapt to the harsher site environment; the most suitable application Factory automation, machinery manufacturing, numerical control equipment, textile equipment, intelligent power, food traceability and other host computer monitoring and control.

PPC-P133-HY is compatible with mainstream operating systems and embedded operating systems such as Windows7, Windows10, Linux, etc. It can run application software and programs based on the above operating systems independently developed by customers, and install industrial automation configuration software to form a powerful man-machine interface.

Feature:

13.3" true color LCD display, resolution 1920x1080, backlight service life up to 50,000 hours

The front panel reaches IP65 protection level to prevent dust and splashed water from entering the display

Ultra-thin design, save cabinet space, shock and vibration resistance

9～36V wide-voltage DC power input, which meets industrial field supply

Electric high-precision capacitive screen, with many industrial field application characteristics

Support panel embedded and standard VESA installation at the same time, users can flexibly choose the installation method

Specification:                       PPC-P133-HY

| System parameters | CPU | J1900/I5-4200U processor |
| --- | --- | --- |
|  | RAM | Onboard 4GB DDR3 (expandable) |
|  | Disk | Support MSATA / SSD and SATA2.5 "notebook hard drives |
| I/O interface | Network port | 2 x Intel Gigabit Ethernet |
|  | Audio | RTLALC662 audio controller, LINE-out port |
|  | USB | 3/4 x USB3.0 |
|  | Serial port | 3/6 x RS232/(2 can be set to RS485/RS422) |
|  | GPIO | 14 channels (custom) |
| LCD screen | Display | 13.3”TFT LED |
|  | Resolution | 1920x1080 |
|  | Brightness | 350cd/m2 |
|  | Contrast | 800:1 |
|  | Maximum color | 16M |
| Touch screen | Types of | Capacitive |
|  | Click life | 250 grams of force, 50 million times |
|  | Response time | <5ms |
|  | Transmittance | above 91% |
|  | High temperature test | 85℃/1000hrs |
|  | Constant temperature and humidity test | 85℃/90%RH/1000hrs |
| Mechanism parameters | Panel cabinet | Aluminum profile face frame |
|  | Installation method | Wall mount |
|  | Power input | 9～36V DC power supply |
|  | Overall dimensions | 338mmx215mmx43mm |
|  | Power | 30W |
|  | Weight | 2KG |
| Environmental parameters | Operating temperature | -20～60℃（Electronic disk） |
|  | Storage temperature | -30～80℃ |
|  | Front panel protection | IP65 standard |

Ordering Information:

| Product number | Configuration |
| --- | --- |
| PPC-P133-HY/J1900 (economical type) | J1900/2 x RJ-45/3 x USB/2 x RS232/12v |
| PPC-P133-HY/J1900 (industrial type) | J1900/onboard 4G/2 x RJ-45/4 x USB/4 x RS232+1 x RS485+1 x (RS232/422/485)/optional 9-36V |
| PPC-P133-HY/I5-4200U (industrial type) | I5-4200U/onboard 4G/2 x RJ-45/4 x USB/4 x RS232+1 x RS485+1 x (RS232/422/485)/optional 9-36V |

Dimensions:

Contact:

Allen Dai / Sales Manager

Armortec Technology Limited

Email: allen.y.dai@armortec.net

Skype: allen.dai89

Tel: +86 150 1266 9595